## Slide 1: Assignment #2: High aspect ratio MEMS Marc Johannes Aslan, Thomas Kötzner

## Slide 2: Assignment
state the assignment
General remarks:
when using images which are not yours, state the source (either directly underneath the image or in the foot of the page)
stick to the font size
avoid over-crowding the page
the total length of the presentation should be 10 minutes (usually around 5-6 content slides)
cold run your presentation before you give the take in the plenum to make sure you stick to the time and that the presentation works

## Slide 3: Assignment
high aspect ratio MEMS devices are required for a number of common applications
name a few of the applications where high-aspect ratio structures are required
what methods are available to make high aspect ratio MEMS structures
  in metals
  in polymers
  in semiconductor materials

## Slide 4: High aspect ratio
Definition: ratio between the depth and minimal lateral expansion
Bigger 10:1
Advantages:
  High packaging density
  Flexibility in 3 dimensions
  Structures of different shapes and varying heights or widths
    Thick high mass elements
    Released features
    Increased capacities
Limitations:
  Depending on fabrication process
  mechanical effects (e.g weight, inertial, angles etc.)
  Costs, design and planning

## Slide 5: Applications
Micro inertial sensors:
  Gyroscopes
  Accelerometers
  Angular rate sensors
Nano tubes
3D circuit integration
Plenty of further applications
Notes: Ende: Überleitung nicht alles Prozesse werden vorgestellt

## Slide 6: Fabrication Methods - Metals
Lithographie, Galvanik und Abformung (LIGA)
X-ray LIGA (high aspect ratio) and UV-LIGA
  Lithography
  Exposure
  Development
  Electroplating
  Stripping
Also applicable to polymeres and semiconductor materials
Aspect ratios > 100:1 possible

## Slide 7: Fabrication Methods - Polymers
Hot embossing
  Prdoucing Embossing master by LIGA or DRIE
  Heating up Polymer
  Embossing
  Cooling down
Specialised for Polymers
Applications e.g. for medicine
Very cheap process

## Slide 8: Fabrication Methods - Semiconductors
Deep Reactive Ion Etching (DRIE)
  Passivation with polymers
  Open the passivation layer at the bottom
  Etching silicon at the bottom
UV LIGA
SCREAM