## Slide 1: Assignment #2: High aspect ratio MEMS Marc Johannes Aslan, Thomas Kötzner

## Slide 2: Assignment
high aspect ratio MEMS devices are required for a number of common applications
name a few of the applications where high-aspect ratio structures are required
what methods are available to make high aspect ratio MEMS structures
  in metals
  in polymers
  in semiconductor materials

## Slide 3: High aspect ratio
Definition: ratio between the depth and minimal lateral expansion
Bigger 10:1
Advantages:
  High packaging density
  Flexibility in 3 dimensions
  Structures of different shapes and varying heights or widths
    Thick high mass elements
    Released features
    Increased capacities
Limitations:
  Depending on fabrication process
  mechanical effects (e.g weight, inertial, angles etc.)
  Costs, design and planning
Notes: - Harm is defined bigger than 10:1
High packaging density: can use the hight rather than the area
Releasd features: fixd on several pionts but e.g kind of hovering in the middle (no contact to the substrade
Increase capacites: sensors detect chances in in some internal capacities -> easier to detect those in bigger
Not every process is can reach the same aspect ratio mentiond in futher piont of the presentation
Mechanical effects: own weigth, inertial (Trägheit), angle to ground plate ( to high and to much angle -> it will tillt

## Slide 4: Applications
Micro inertial sensors:
  Gyroscopes
  Accelerometers
  Angular rate sensors
Nano tubes
3D circuit integration
Plenty of further applications
Hutchison et al., Carbon nanotubes as a framework for high-aspect-ratio mems fabrication, Journal of Microelectromechanical Systems, 2010
Notes: Johannes
There are so many different applications for microstructures with High aspect ratio
One big area of applications is micro inertial sensors
Application in automotive, smartphone etc.
With high aspect ratio it is possible to increase the sensivity of those sensors
Nanotubes: framework for builing microstructures with HAR
3d circuit integration: high aspect ratio for circuit paths
And so on
Ende: Überleitung nicht alles Prozesse werden vorgestellt

## Slide 5: Fabrication Methods - Metals
Lithographie, Galvanik und Abformung (LIGA)
X-ray LIGA (high aspect ratio) and UV-LIGA
  Exposure
  Development
  Electroplating
  Stripping
Also applicable to polymeres and semiconductor materials
Aspect ratios > 100:1 possible
Menz et al., Mikrosystemtechnik für Ingenieure, John Wiley & Sons, 2012
Notes: Johannes
German Name, developed in Germany: Lithography, Galvanik und Abformung
Steps are:
  Lithography
  Application conductive seed layer on substrate (any metals, if needed: adhesive) _> sputtering or evaporation
  Adding photoresistive material
  exposure with X-ray by synchrotron source
  Developing the resist
  Electroplating
  Filling remaining resist upwards from seedlayer with metal
  Stripping
  Remove remaining resist chemical
Also usable for polymers and semiconductor materials
High aspect ratios over 100:1 possible

## Slide 6: Fabrication Methods - Polymers
Hot embossing
  Producing Embossing master by LIGA or DRIE
  Heating up Polymer
  Embossing
  Cooling down
Specialised for Polymers
Applications e.g. for medicine
Very cheap process
Becker et al., Hot embossing as a method for the fabrication of polymer high aspect ratio structures, Sensors and Actuators A: Physical, 2000
Notes: Process special for polymers
Hot embossing:
  Produce embossing master by Liga or DRIE, works like a stamp, must be high quality
  Then heating up the polymer
  Embossing the polymer, embossing tool borught to contact with preheated polymer and embossed into it
  Remove tool
  Cooling down polymer
Possible to use all advantages of polymers for MEMS
Example BioMEMS, Medicine
High aspect ratios possible
Very cheap compared to other processes

## Slide 7: Fabrication Methods - Semiconductors
Deep Reactive Ion Etching (DRIE)
  Passivation with polymers
  Open the passivation layer at the bottom
  Etching silicon at the bottom
UV LIGA
SCREAM
[Fraunhofer ISIT. (2019) Deep reactive ion etch (drie). Accessed January 30, 2019.[On-line]. Available:https://www.isit.fraunhofer.de/de/technologie/mikrofertigungsverfahren/waferbearbeitung/deep-reactive-ion-etch.html
Notes: DRIE ( deep reactiv ion etching)
-50:1
-cost savings and faster process time
-etching into the substrade
-passivation plasma-polymer-layer (isotropic)
-etch next step through the layer into substrade (anisotorpic)
-disadvantage of this process is the litigation. It has to be optimized for every single structure, to get vertical and smooth side walls
-aufs bild verweisen
UV LIGA
- enhancement of X-Ray LIGA
- uses photoresist enabled the fabrication without synchrotron source
- not so precisly like normal liga, but cheaper
SCREAM (Single Crystal silicon Reactive Etching an Metallization)
- 50:1
- under etched structures like beams and bridges
- uses DRIE but Silicon oxide an an isotropic etch process to undermine the trenches.
- very large, robust and stiff vertical movable structure
- low quality factor because of high damping of the silicon dioxide layers
- thermal stress because of different materials which are used